## Slide 1
Floating Content in Vehicular Ad-hoc Networks
Gaetano Manzo, Ph.D. Student
University of Bern & University of Applied Sciences Western Switzerland
Annual meeting Bern 21/07/2017

## Slide 2: Storyboard
Floating Content in VANETs
Random Waypoint to model FC
(ITC)
Anchor Zone reshape for saving resources
(MobiWorld)
Hybrid scenario
Several vehicular traces
Machine Learning approach
Past work
Present / Future

## Slide 3
Floating Content (FC) is a possible solution to lead the information spreading in the vehicular environment.

## Slide 4: Anchor Zone Opportunistic communication Mobility model Application
FC is a possible solution!
Information geographically constrained
No infrastructure support needs
Suitable for vehicular and pedestrian scenario
Attractive for
Advertisement
Safety
. . .
SLOW DOWN !

## Slide 5: Floating Content
Basic Functionalities

## Slide 6: Content generation Content spreading Content erasing
Node = =
or
node deleting the content
node without the content
node with the content

## Slide 7: Random waypoint has been used to model FC in vehicular scenario
G. Manzo, M. A. Marsan, and G. A. Rizzo, ”Performance modeling of vehicular Floating content in urban setting” - ITC Conference 2017.

## Slide 8: We define the “District Model” to characterize the AZ It is not our concern to model the world outside the AZ
Within AZ:
District Model
Outside AZ:
Arbitrary Mobility
Arbitrary Mobility
Arbitrary Mobility
Arbitrary Mobility

## Slide 9: The District Model is an extension of the RWP Mobility Model
enter
exit
RWP
Assumption: all pdf are the same!
waypoint
Within the AZ nodes move (Tmove) according to RWP with pause (Tstop)

## Slide 10: Our process is easy!
Study of an epoch
System performance
Assumptions
Tmove
Tstop
Node uniform distributed
Poisson arrival time
No border effect
No clustering
Success probability
Availability
Floating Content

## Slide 11: Numerical evaluation has been done in ad-hoc and real scenario
1000m
Ad-hoc simulation to assess the analytical part
Model evaluated on vehicular environment

## Slide 12
The high correlation between model and ad-hoc simulation shows the marginal impact of the assumptions made

## Slide 13
The success probability is strongly correlated with the mobility within the AZ
District: Residential; City center; Industrial.

## Slide 14: If the content does NOT float the success probability is a useless perfomace parameter!

## Slide 15: Sojourn time, node density are the principal parameters Floating<2 min Low density Floating<40 min High density, short sojourn time Floating>2 hours Medium density, long sojourn time
R
DISTRICT
C
DISTRICT
I
DISTRICT
Low traffic time data:

## Slide 17: Floating Content modelization Future work

## Slide 18: The next step of this work is simulate several scenarios
Hybrid :
Pedestrian & Vehicular
Several vehicular mobility trace
e.g., Bologna and Helsinki traces
Manhattan
Cologne
Lux (several zones)
…

## Slide 19: Anchor Zone dimensioning is still an open challenge
G. Manzo, R. Soua, A. Di Maio, T. Engel, M. R. Palattella, and G. Rizzo, ” Coordination Mechanisms for Floating Content in Realistic Vehicular Scenario” - MobiWorld 2017, IEEE INFOCOM.

## Slide 20
By leading the Anchor Zone radius is possible to control the number of nodes involved in the communication.

## Slide 21: There are several performance parameters to optimaze in order to save resources
#nodes with content
#nodes exiting with content
Content lifetime
Time to get the content
Find the minimum AZ radius which respect the success probability desired

## Slide 22: FC performance is modelled by the RWP mobility model to evaluate the minimum radius

## Slide 23: The estimation of vehicular density parameter is required as input for the chosen mobility model
By the city map: Tstop and Tmove
Two different approaches to estimate node density:
Centralized: infrastructure-supported
Distributed: infrastructure-less

## Slide 24
Infrastructures support node density estimation in the centralized approach

## Slide 25
The distributed approach is used for infrastructure-less situation
SECTOR
SECTOR

## Slide 26
The estimation has to be computed by vehicles, possible in a cooperative way
More sectors the higher is the quality of the estimation

## Slide 27: The choice of the number of the sectors to estimate node density is a thread-off between accuracy and payload.
The right number of sectors is not trivial choice

## Slide 28
Simulation Setting
Tstop 15s, Tmove 25s
AZ placed in C
Node TX range radius 100m
Simulation time:
3h for low-traffic (4am-6am)
and high-traffic (7am-9am)

## Slide 29
Unlike peak traffic time, the simulation results during low traffic show a stable node arrival rate
Low Traffic
Peak Traffic
From node density to arrival rate by the Little’s Law

## Slide 30
Success probability for both approaches during low and peak time traffic reflects the node density estimation
Low Traffic
Peak Traffic

## Slide 31
The increasing of AZ radius does not necessarily involve a higher success probability
Model uniform node density.
Not including traffic zone, success probability does not raise

## Slide 32: A machine learning approach for FC Future work

## Slide 33: The aim is the same of the previous work but the approach is not model-based
INPUT
Output
Previous Work:
MODEL
OPTIMIZATION
Features &
App. requirement
Output
Future Work:
Given by the DATA

## Slide 34: The first step is to select the features (system input)
Mobility & Network Features:
Mean time moving and static (Tmove, Tstop)
Mean arrival rate (lambda)
Node transmission range (r)
Mean speed (v)
Sojourn time (Tsoj)
Application requirement:
Minimum Anchor Zone radius (Rmin)
Maximum Anchor Zone radius (Rmax)
Target Success Probability (TPsucc )
The training set is a table with all the features + success probability + AZ radius
Tmove Tstop lambda r v Tsoj R Psucc
Training set :

## Slide 35: The second step is to train our model
Tmove Tstop lambda r v Tsoj R Psucc
Training set :
Learning Algorithms
Feature 1
Feature 2
Feature n
INPUT

## Slide 36: The last step is to TEST our model
Features set :
Learning Algorithms
Feature 1
Feature 2
Feature n
INPUT
Tmove Tstop lambda r v Tsoj
TPsucc Rmin Rmax
Cost function set :
R that respect the application requirement

## Slide 37
Spreading limitation in LUX city
using a grid

## Slide 38
Spreading limitation in LUX city
using a grid

## Slide 39
Spreading limitation in LUX city
using a grid

## Slide 40: Things to do
Confirm the features and training set
Cross correlation
Choose the way to extract the training set
Choose machine learning technique
Test the machine with real data traffic e.g., LUX trace

## Slide 41
Thank you